## Inter-Integrated Circuit (I2C) group
This group defines all used Inter-Integrated Circuit (I2C) interfaces.
Each I2C interface is a sub group with the I2C name as the group name.
    "I2C": {
        "dac_i2c": {
        "pad_scl": "PA5",
        "pad_sda": "PA6",
        "peripheral" : "I2C0",
        "role": "master",
        "address_bits": "7",
        "clock_max_frequency": "100 kHz",
        }
    }
#### pad_scl
Serial Clock.
type: String
#### pad_sda
serial data signal.
type: String
### peripheral
name of the I2C peripheral to use.
type: String
#### role
Describes the role in the communication. Possible values are:
- master
- slave
type: enum
#### address_bits
7bit Address or 10 bit Address
#### clock_max_frequency
fastest speed (shotest bit time) to use on the SCL line.
- Standard Speed (up to 100 kHz)
- fast mode (up to 400 kHz)
- fast mode plus (up to 1000 kHz = 1 MHz)
- high speed mode (up to 3.4 MHz)
- ultra fast mode (up to 5 MHz)