# EZ-USB FX2G3
USB 2.0 @ 480MHz (High Speed)
Package: 104 LGA
Temperaure range: -45 .. 85 °C
GPIF/FIFO 16bit
## Variants
part #	MCU	SRAM	Flash	SCB #	Peripherals
CYUSB2315-BF104AXI(T)	M0+	512 KB	256 KB	1	I2C
CYUSB2316-BF104AXI(T)	M0+	512 KB	256 KB	3	I2C, SPI, CAN
CYUSB2317-BF104AXI(T)	M0+	512 KB	512 KB	6	I2C, SPI, CAN, QSPI
CYUSB2318-BF104AXI(T)	M4/M0+	1024 KB	512 KB	6	I2C, SPI, CAN, QSPI, Crypto

## Pins
- ePad
- A1..A56
- B1..B48
Pin	Signal name	description
ePAD	GND
A1	P0CTL2
A2	P0CTL1
A3	VDDIOXTAL
A4	XTALOUT
A5	XTALIN
A6	GND
A7	V33
A8	DPLUS
A9	DMINUS
A10	GND
A11	VDDD
A12	GND
A13	P0CLK
A14	Reserved
A15	I2C-SCL0 (SCB0)
A15	UART-RX0 (SCB0)
A16	I2C-SDA0 (SCB0)
A16	UART-TX0 (SCB0)
A17	VDDIO
A18	P0D0
A19	P0D1
A20	P0D2
A21	P0D3
A22	P0D4
A23	P0D5
A24	P0D6
A25	P0D7
A26	GND
A27	VDDIOP0_CTRL
A28	GND
A29	P0CTL5
A30	P0CTL6
A31	P0CTL9
A32	VDDIOP0
A33	GPIO2
A33	UART-TX0
A33	I2C-SDA0 (SCB5)
A33	SPI-CS0 (SCB5)
A33	CAN1-RX
A34	PMODE
A34	SPI-MOSI (SCB5)
A34	CAN1-TX
A35	P0CTL0
A36	GPIO1
A36	UART-RX0
A36	I2C-SCL0 (SCB5)
A36	SPICLK (SCB5)
A37	P0CTL3
A38	P0CTL4
A39	P0CTL7
A40	P0CTL8
A41	GND
A42	XRES
A43	VDDIOP0_CTRL
A44	VBUSDETECTN
A45	P0D8
A46	P0D9
A47	P0D10
A48	P0D11
A49	P0D12
A50	P0D13
A51	P0D14
A52	P0D15
A53	GND
A54	CLKOUT
A55	VDDIOP0
A56	GND
B1	DNU
B2	DNU
B3	DNU
B4	DNU
B5	DNU
B6	DNU
B7	DNU
B8	GND
B9	DNU
B10	DNU
B11	DNU
B12	DNU
B13	DNU
B14	RESREF
B15	TDO / SWO
B15	PDM3-CLK0
B15	UART-TX1 (SCB4)
B15	I2C-SCL1 (SCB4)
B15	SPICLK (SCB4)
B16	TDI
B16	PDM3-DATA0
B16	UART-RX1 (SCB4)
B16	I2C-SDA1 (SCB4)
B16	SPICS0 (SCB4)
B17	TMS / SWDIO
B17	PDM3-CLK1
B17	UART-RTS1 (SCB4)
B17	SPI-MOSI (SCB4)
B18	TCLKSWDCLK
B18	PDM3-DATA1
B18	UART-CTS1 (SCB4)
B18	SPI-MISO (SCB4)
B19	GPIO
B19	SWDRST
B20	PDMDATA
B20	TCPWM4_N
B21	GPIO4
B21	SPI-MISO (SCB5)
B22	SPICLK (SMIF)
B22	UART-RX1 (SCB6)
B22	I2C-SCL1 (SCB6)
B23	SPICS0 (SMIF)
B23	UART-TX1 (SCB6)
B23	I2C-SDA1 (SCB6)
B24	SPICS1 (SMIF)
B25	CAN0-TX
B25	PDM0-DATA1
B25	UART-TX0 (SCB4)
B25	I2C-SDA0 (SCB4)
B25	TCPWM2_N
B25	SPICS0 (SCB4)
B26	CAN0-RX
B26	PDM0-CLK1
B26	UART-RX0 (SCB4)
B26	I2C-SCL0 (SCB4)
B26	TCPWM2_P
B26	SPICLK (SCB4)
B27	SPIDAT0 (SMIF)
B27	UART-RX1 (SCB0)
B27	I2C-SCL (SCB0)
B27	SPICLK (SCB2)
B28	SPIDAT1 (SMIF)
B28	UART-TX1 (SCB0)
B28	I2C-SDA (SCB0)
B28	SPICS0 (SCB2)
B29	SPIDAT2 (SMIF)
B29	UART-CTS0 (SCB0)
B29	SPI-MOSI (SCB2)
B30	SPIDAT3 (SMIF)
B30	UART-RTS0 (SCB0)
B30	SPI-MISO (SCB2)
B31	VDDIOQSPI
B32	SPIDAT4 (SMIF)
B32	UART-CTS0 (SCB2)
B33	SPIDAT5 (SMIF)
B34	SPIDAT6 (SMIF)
B34	UART-RX1 (SCB1)
B34	I2C-SDA1 (SCB1)
B35	SPIDAT7 (SMIF)
B35	UART-TX1 (SCB1)
B35	I2C-SCL1 (SCB1)
B36	DNU
B37	DNU
B38	GPIO5
B39	GPIO6
B40	VCCD
B41	DNU
B42	GPIO8
B43	GPIO9
B44	PDMCLK
B44	TCPWM4_P
B45	GPIO10
B46	USB2DN2
B47	USB2DP2
B48	DNU

## abbreviation dictionary
abbreviation	long version	comment
DNU	Do not use	Do not use these connections for PCB signal routing channels. Do not connect any host system signal to these connections.
NC	Not connected	The connection may safely be used for routing space for a signal on a PCB. However, any signal connected to an NC pin must not have voltage levels higher than VIO.
RFU	Reserved for Future use	Do not use RFU connectors for PCB routing channels so that the PCB may take advantage of future enhanced features in devices with a compatible footprint.
SCB	Serial Control Block	A peripheral that can be used as I2C, UART or SPI