# command k
Format: ‘k’
Meaning: Kill request.
The exact effect of this packet is not specified.
For a bare-metal target, it may power cycle or reset the target system. For that reason, the ‘k’ packet has no reply.
For a single-process target, it may kill that process if possible.
A multiple-process target may choose to kill just one process, or all that are under GDB’s control. For more precise control, use the vKill packet (see vKill packet).
If the target system immediately closes the connection in response to ‘k’, GDB does not consider the lack of packet acknowledgment to be an error, and assumes the kill was successful.
If connected using target extended-remote, and the target does not close the connection in response to a kill request, GDB probes the target state as if a new connection was opened (see ? packet).
Reply: no reply !