# SPI
Different variants exist. Usually SPI refers to the Motorola Serial Peripheral Interface. Other variants are the Texas Instruments Serial protocol (SSP) and the National Instruments Microwire.
## Protocol
Most significant bit first
## Modes
There are 4 Modes. Defied by the two settings “clock polarity” CPOL and “clock phase” CPHA.
“clock polarity” CPOL = 0:
Clock line is low when idle.
“clock polarity” CPOL = 1:
Clock line is high when idle.
“clock phase” CPHA = 0:
1. first data bit is output on /CS activating (going low).
2. data bits change when clock goes to idle level.
3. data bits are read when clock comes from idle level.
“clock phase” CPHA = 1:
1. first data bit starts on first edge after /CS activates.
2. data bits change when clock comes from idle level.
3. data bits are read when clock goes to idle level.
mode	CPOL	CPHA	write bit	read bit
0	0	0	clock goes low, and when /CS activates	clock goes high
1	0	1	clock goes high	clock goes low
2	1	0	clock goes high, and when /CS activates	clock goes low
3	1	1	clock goes low	clock goes high

## SPI group
This group defines all used Serial Peripheral Interface (SPI) interfaces.
Each SPI interface is a sub group with the SPI name as the group name.
    "SPI": {
        "encoder_spi": {
        "pad_sck": "PA5",
        "pad_miso": "PA6",
        "pad_mosi": "PA7",
        "pad_ncs": "PA15",
        "peripheral" : "SPI0",
        "role": "master",
        "communication_mode": "duplex",
        "frame_format": "motorola",
        "clock_polarity": "idle_low",
        "clock_phase": "sample_on_leading_edge",
        "bit_order": "msb_first",
        "baud_rate": "10 MHz",
        }
    }
#### pad_sck
Serial Clock.
type: String
#### pad_mosi
“Master Out Slave In” data signal.
type: String
#### pad_miso
“Master In Slave Out” data signal.
type: String
#### pad_ncs
Chip Select signal (Low active).
type: String
### peripheral
name of the SPI peripheral to use.
type: String
#### role
Is either master(host) or slave(device).
type: enum
default: master
#### communication_mode
Describes the communication. Possible values are:
- duplex : the traditional mode using MISO and MOSI to transmit and receive at the same time.
- half-duplex : meaning the same wire between master and slave is used for both directions.
- receive-only : send line is not used
- send-only : receive Line is not used.
type: enum
default: duplex
#### frame_format
Describes the communication. Possible values are:
- motorola : the “normal” SPI.
- ti :
type: enum
default: motorola
#### clock_polarity
Also often called CPOL. Describes the communication. Possible values are:
- idle_low
- idle_high
type: enum
default: idle_low
#### clock_phase
Also often called CPHA. Describes the communication. Possible values are:
- sample_on_leading_edge : samples the data on the edge from idle value to non-idle value.
- sample_on_trailinging_edge : samples the data on the edge from non-idle value to idle value.
type: enum
default: sample_on_leading_edge
#### SPI Mode
Sometimes the documentation talks about a SPI Mode with the value of 0 to 3. This mode maps to the phase and polarity as described in the following table:
Mode	CPOL	CPHA	description
0	0	0	clock: idle_low, phase: sample_on_leading_edge
1	0	1	clock: idle_low, phase: sample_on_trailing_edge
2	1	0	clock: idle_high, phase: sample_on_leading_edge
3	1	1	clock: idle_high, phase: sample_on_trailing_edge

#### bit_order
Describes the communication. Possible values are:
- msb_first : most significant bit first (bits on the line : 76543210 )
- lsb_first : least significant bit first (bits on the line: 01234567 )
type: enum
default: msb_first
#### baud_rate
Is the number of bits per second exchanged on the data lines. Expressed as frequency of the clock line.
type: int (Hz)
## API
The part “signal_name” in the described functions will be replaced by the name of the signal. E.g. if your signal is called “audio” then the API function “signal_name_transfer” will become “audio_transfer”.
void signal_name_transfer(const uint8_t *data_send,
        const uint8_t *data_receive,
        const uint32_t length )
Will send “length” bytes from the buffer “data_send” out on MOSI and will receive the same amount of bytes from MISO into the buffer “data_receive”.